## Slide 1: Microsoft 365 Network Connectivity Video Series Enterprise network design for the cloud era
Paul Collinge
Senior Program Manager – Microsoft 365
July 2020

## Slide 2: Microsoft 365 Network Connectivity Principles
Optimize Microsoft 365 traffic Use the endpoint categories to differentiate Microsoft 365 traffic from generic Internet traffic for more efficient routing.
aka.ms/o365ip
Enable local egress Egress Microsoft 365 data connections through Internet as close to the user as practical with matching DNS resolution.
Enable direct connectivity Enable direct egress for Microsoft 365 connections. Avoid network hairpins and minimize network latency (RTT) to Microsoft’s global network.
Modernize security for SaaS Avoid intrusive network security for Microsoft 365 connections. Assess bypassing proxies, traffic inspection devices, and duplicate security already available in Microsoft 365.
ISP
SSL B&I
Microsoft 365 endpoints
{REST:API}
Datacenter
Learn more at: aka.ms/PNC

## Slide 3: The enterprise connectivity challenge
Enterprise last mile
Enterprise last mile
Head Office
ISP
On premises network
Proxy Server
Firewall / NGFW
Branch Office
On premises network
Corporate MPLS WAN / Network perimeter
MPLS
Secure Web Gateway
Data Loss Prevention
Intrusion Prevention System
Firewall / NGFW
Cloud Access Security Broker
WAN Accelerator
Home Office
VPN
Hotel
Coffee shop
Proxy Server
Microsoft global network
Network first mile
Network first mile
Network first mile
Windows/Office Updates
Network first mile
Other Cloud Services

## Slide 4: Traditional network architecture MPLS backhaul to central proxied egress/security stack
Internet Proxy
DLP
IPS
Firewall
MPLS/WAN
Router
Singapore Head office
Sydney Branch office
Users PC
Singapore Service
Front Door
Router
Common results:
Latency to Microsoft 365 Front Door = 140ms
High Load on centralized egress impacting web browsing and other business critical use
High load on MPLS circuit, impacting all other business critical use
High cost of international backhaul on MPLS circuit
Poor ability to adapt to changing needs/requirements
Poor quality Teams Calls & Meetings
Sluggish Outlook behavior
Slow file transfer to/from OneDrive for Business

## Slide 5: Modern network architecture: Example #1 SDWAN for direct Microsoft 365/Azure public endpoints – reduced/removed MPLS load/costs
MPLS/WAN
Internet Proxy
DLP
IPS
Firewall
1
2
SDWAN device
Singapore Head office
Sydney Branch office
Users PC
SDWAN local branch egress
SDWAN device used for local ISP breakout
For Office 365, the device can auto consume the ‘Optimize’ category from the web service
Other desired traffic such as update traffic and trusted & defined cloud services can use this path
Azure Public endpoints can also be accessed directly through this method
Standard corporate network security stack
Other traffic goes direct to standard internet browsing path
This is the remainder of Microsoft 365 URLs.
Also any other browsing traffic
1
2
ISP 1
ISP 2
Windows/Office Updates
Other Cloud services
SDWAN device
Singapore Service
Front Door
Common results:
Latency to Microsoft 365 Front Door = 10ms
Removed load on centralized egress
Reduced load on MPLS circuit, allowing capacity for all other business critical use
MPLS circuit can feasibly be downsized or removed over time, reducing cost
High ability to adapt to changing needs/requirements
High quality Teams Calls & Meetings
Highly responsive Outlook functions
High speed OneDrive for Business transfers
Australia Service
Front Door

## Slide 6: Modern network architecture: Example #2 SDWAN for Office 365 egress through Secure Web Gateway
Legacy Egress
DLP
IPS
Firewall
2
Singapore Head office
SDWAN used to send all traffic via a Cloud based, Secure Web Gateway
SDWAN device used for local ISP breakout
Most traffic is sent to the nearest secure web gateway
Trusted endpoints such as Office 365 ‘Optimize list’ are sent direct
Corporate traffic can be sent direct to Head Office via SDWAN or via SWG
Standard corporate network security stack
Legacy egress kept in place for edge cases
1
2
Windows/Office Updates
Other Cloud services
1
SDWAN device
Auckland Branch Office
Users PC
1
SDWAN device
Sydney Branch Office
Users PC
Cloud based Secure Web Gateway – Sydney Node
SDWAN device
Internet
Australia Service
Front Door
NZ Service
Front Door
Singapore Service
Front Door
2

## Slide 7: Zero Trust
Identities - Verify and secure each identity with strong authentication across your entire digital estate.
Devices - Gain visibility into devices accessing the network. Ensure compliance and health status before granting access.
Applications - Discover shadow IT, ensure appropriate in-app permissions, gate access based on real-time analytics, and monitor and control user actions.
Data - Move from perimeter-based data protection to data-driven protection. Use intelligence to classify and label data. Encrypt and restrict access based on organizational policies.
Infrastructure - Use telemetry to detect attacks and anomalies, automatically block and flag risky behavior, and employ least privilege access principles.
Network - Ensure devices and users aren’t trusted just because they’re on an internal network. Encrypt all internal communications, limit access by policy, and employ micro segmentation and real-time threat detection.

## Slide 8
Azure AD conditional access
Application
Per app policy
Client type (Web, Rich, mobile)
Cloud and On-premises applications
User attributes
User id
Group membership
Devices
Domain Joined
Compliant
Platform type (Windows, iOS, Android)
Location
IP Range
ADFS
Risk
Session risk
User risk
ENFORCE MFA
ALLOW
BLOCK
Enroll
Maintain control in the cloud-first mobile-first world

## Slide 9: Tenant restrictions
Service
Front Door
Internet Proxy with Tenant Restrictions Enabled
Firewall
1
2
MPLS/WAN
SDWAN device
Head office
Branch office
Users PC
SDWAN local branch egress
Connections to Optimize marked endpoints sent direct to the service via local breakout
1
ISP 1
ISP 2
Azure AD
SDWAN device
2
Authentication traffic sent via proxy with Tenant Restrictions enabled
Proxy has a preconfigured list of approved tenants
If Authentication is not against an approved tenant, no token is issued
If Authentication is against an approved tenant, token is issued if correct to do so

## Slide 10: Additional resources and recommended actions
View our Microsoft 365 Network Connectivity video series page
Evaluate your network for SaaS cloud readiness
Invest to optimize for performance and user experience
Microsoft 365 Network Connectivity Principles:
  Incorporate in your network designs for office and remote workers
  Use to evaluate network solutions and services
Use Microsoft 365 tools to monitor for network score