## Slide 1: Architect and simplify hybrid networking with Azure Virtual WAN and SD-WAN
Reshmi Yandapalli
Principal Product Manager, Azure Networking

## Slide 2: Agenda
1.
2.
3.
4.
5.
6.
Azure Virtual WAN Overview
Key Partner announcements
Monitoring
Transit Routing use cases
Integrated Network Virtual Appliance (Demo)
Summary

## Slide 3: Azure Virtual WAN overview
Unified framework for networking, security and routing
Routing
Global transit architecture
Secure virtual hub
Integrated network virtual appliance
Connectivity

## Slide 4: Azure Virtual WAN Overview
Routing
Global transit architecture
Secure virtual hub
Integrated network virtual appliance
Connectivity
Site-to-site VPN
  Supports IKEv1, IKEv2 protocol
  VPN/SD-WAN CPE partnerships with signed agreements for configuration and connectivity automation
  Scale : Up to 1000 connections/region (hub), 20 Gbps aggregate throughput /region (hub)
  New : FQDN based IPsec, custom BGP/APIPA
Point-to-Site VPN
  Support IKEv2, OpenVPN protocol, cert based and RADIUS authentication
  Built in traffic management, Integrated with Azure VPN Client
  Scale : Up to 10K users/region (hub ), 20 Gbps aggregate throughput /region (hub)
  New : Custom DNS
Private Connectivity with ExpressRoute
  Support encryption with native site-to-site VPN
  Scale : Up to 20 Gbps aggregate throughput /region (hub)
  New : Up to 8 circuit connection per region (hub), ), Ability to connect Standard circuits

## Slide 5: Virtual WAN Partners
Coming Soon
MSP Partners providing Azure Virtual WAN Services
VPN/SD-WAN Device Connectivity automation with Virtual WAN VPN
Partners with Azure Marketplace based network virtual appliance deployable in Virtual WAN hub
Viptela
SD-WAN
SD-WAN
Coming Soon
Notes: Growing number of Telcos and SIs are now offering Managed Services for Virtual WAN​
Services include:​
Plan, Design, Implementation and Operations of Enterprise Hybrid Networks based on Virtual WAN ​
Integration with Enterprise SD-WAN​
Non-DIY Enterprises could leverage these Partner offerings to build and operate their Virtual WAN ​
For a full list of offers: See Azure Networking MSP Partners ​

## Slide 6: Azure Virtual WAN Overview
Routing
Global transit architecture
Secure virtual hub
Integrated network virtual appliance
Connectivity
Fully meshed hub
Any-to-any connectivity
  Branch to Azure
  Branch to branch
  Users <->Branch
  VNet<->VNet transit
  VPN<-> ExpressRoute transit

## Slide 7: Azure Virtual WAN Overview
Routing
Global Transit Architecture
Secure Virtual Hub
Integrated Network Virtual Appliance
Connectivity
Virtual Hub Router
  One router per virtual hub
  Controls routes between all gateways
  Provides VNET<->VNET transit
  Scale : Up to 50 Gbps aggregate throughput /region (hub) for VNet to VNet transit connectivity, Up to (500 minus #Hubs) VNet Spoke connections to each hub
Custom Routing
  Custom Route table for VNETs
  Default Route Table for Branches (P2S, S2S, ER)
  Associate Connections to route tables
  Propagate routes from Connections to route tables
  View effective routes on route tables
Virtual Hub Router
VPN Gateway
ExpressRoute Gateway
User VPN Gateway
Azure Firewall

## Slide 8: Azure Virtual WAN Overview
Routing
Global transit architecture
Secure virtual hub
Integrated network virtual appliance
Connectivity
Secure a Virtual Hub with Azure Firewall
Secure with Security-as-a-Service (SECaaS) partners
  Supported Partners : zScaler, iBoss, CheckPoint
  Set up security policies in Azure Firewall Manager
Azure Firewall Manager
  Create policy and apply across multiple firewalls
  Works across regions/subscription/deployments
  Secure Internet traffic (VNET ->Internet and Branch ->Internet)
  Secure Private traffic (VNET <->Branch)
HQ/ branch
Datacenter
Remote User
Azure VNet
Internet
Secure Virtual Hub

## Slide 9: Azure Virtual WAN Overview
Routing
Global transit architecture
Secure virtual hub
Integrated network virtual appliance
Connectivity
Deploy Azure Marketplace NVA (BYOL/PAYG)
  Supported Partners : Barracuda, Cisco Viptela (New)
Integrated with Virtual WAN
  Supports transit scenario of SDWAN <-> Azure VPN Site, Remote User, ExpressRoute
  Secure Access Service Edge (SASE) with Secure Virtual Hub (Virtual Hub with Azure Firewall)
  Built-in resiliency (no management overhead)
  No hassle routing – Integrated with Virtual Hub Router
  Supports Network Virtual Appliance Provider’s proprietary features (e.g. Configure SD-WAN policies)
Virtual Hub Router
VPN Gateway
ExpressRoute Gateway
User VPN Gateway
Azure Firewall
NVA

## Slide 10: Putting it together
Fully meshed hubs
ExpressRoute User
S2S User
P2S User
VNet
VNet
Internet
vWAN scale
8 ckt/Hub
20 Gbps agg
10,000/Hub
20 Gbps agg
1,000/Hub
20 Gbps agg
500/Hub
50 Gbps agg
V<->V
ExpressRoute
User/P2S VPN
Site/S2S VPN
VNet
Connectivity & Security
Azure FW
vWAN
routing
enabled capabilities
Microsoft managed hub
Virtual Hub Router – automatic hub to hub
Virtual Hub Router – Fully meshed hubs
Transit between VPN and ExpressRoute, VNETs
Custom Routing
Integrated Network Virtual Appliance (NVA)
S2S connectivity automation
FW Manager Partners
vWAN unique
ER
Encryption
P2S Traffic mgmt
P2S User
VNet
VNet
S2S User
vWAN pricing
VPN, ER
Throughput : $/scale unit
Connection : $/conn unit
FW : Per hr, Per GB
Virtual Hub : Per hr, Per GB
Hub to hub : Source Destination based Egress only charges
Unified framework for networking, security and routing using the Microsoft Global Backbone

## Slide 11
Topology of your network
Metrics
Virtual WAN Monitoring Insights (Preview)

## Slide 12: Transit Routing Use Cases

## Slide 13: Connection, association & propagation
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
Connections propagate routes to route table
VPN Connection
ExpressRoute Connection
P2S Config Connection
Virtual Network Connection
Every hub has a Default Route Table
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | P2S VPN Conn ID
10.1.0.0/24 | VNet 1 Conn ID
10.2.0.0/24 | VNet 2 Conn ID
Enables any-to-any connectivity | 
Default route table | 
Route | Next hop
Connections learn routes from associated route table

## Slide 14: Custom routes, static routes, next hop
Route | Next hop
192.168.0.0/16 | VNet 3 Conn ID
Route | Next hop
10.2.0.0/24 | VNet 2 Conn ID
VNETs can associate to custom route tables
192.168.1.0/24
192.168.2.0/24
192.168.3.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
Route | Next hop
10.1.0.0/24 | VNet 1 Conn ID
RT_VNET | 
Route | Next hop
Add a static route to route table
Add a next hop for 10.3.0.5 in VNet3 connection
VNet3
10.3.0.0/24
10.3.0.5

## Slide 15: Custom use case – Isolating VNets
10.1.0.0/24 | VNet 1 Conn ID
10.2.0.0/24 | VNet 2 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
Default Route Table | 
Route | Next hop
Custom Route Table RT_VNET | 
Route | Next Hop
192.168.1.0/24
192.168.2.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
Branches <->Branches
Branches <->VNet
No VNet <->VNet

## Slide 16: Custom use case – Isolating VNets
10.1.0.0/24 | VNet 1 Conn ID
10.2.0.0/24 | VNet 2 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
Default Route Table | 
Route | Next hop
Custom Route Table RT_VNET | 
Route | Next Hop
192.168.1.0/24
192.168.2.0/24
VNet1
10.1.0.0/24
10.2.0.0/24
Branches <->Branches
Branches <->VNet
No VNet <->VNet
VNet2

## Slide 17: Custom use case – Route to shared services VNets
10.1.0.0/24 | VNet 1 Conn ID
10.2.0.0/24 | VNet 2 Conn ID
10.3.0.0/24 | VNet 3 Conn ID
10.3.0.0/24 | VNet 3 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
Default Route Table | 
Route | Next hop
Custom Route Table RT_VNET | 
Route | Next Hop
192.168.1.0/24
192.168.2.0/24
VNet2
10.1.0.0/24
10.2.0.0/24
Branches <->Branches
Branches -> VNET3
Branches -> VNET1,2
VNETs 1, 2 -> VNET3
VNet1
VNet3
10.3.0.0/24
Shared Services VNET
10.3.0.5
Add a next hop for 10.3.0.5 in VNet3 connection

## Slide 18: Custom use case – Custom isolation VNets
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24
192.168.2.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
Branches <->Branches
Blue Vnets <->Branches
Pink Vnets <-> Branches
Blue VNets <-> Blue VNets
Pink VNets <-> Pink VNets
Branches <-> Blue and Pink VNets
192.168.3.0/24
192.168.4.0/24
VNet3
VNet4
10.3.0.0/24
10.4.0.0/24
Default Route Table – Label Default | 
Route | Next hop
Default Route Table – Label Default | 
Route | Next hop
Custom Route Table – Label Blue | 
Route | Next hop
Custom Route Table – Label Pink | 
Route | Next hop

## Slide 19: Custom Use Case – Multi-hub and any-to-any
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
Default Route Table – Label Default | 
Route | Next hop
Default Route Table – Label Default | 
Route | Next hop
192.168.1.0/24
192.168.2.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
192.168.3.0/24
192.168.4.0/24
VNet3
VNet4
10.3.0.0/24
10.4.0.0/24
Any-to-any
Routing configuration – VNETs , Branches
Association default
Propagation default

## Slide 20: Custom use case – Azure internet edge with Azure Firewall
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
Default Route Table – Label Default | 
Route | Next hop
Default Route Table – Label Default | 
Route | Next hop
192.168.1.0/24
192.168.2.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
192.168.3.0/24
192.168.4.0/24
VNet3
VNet4
10.3.0.0/24
10.4.0.0/24
VNET -> Internet via AzFW
Branch -> Internet via AzFW
Private traffic (VNet, Branch) to go Direct
Add a static route to route table
0.0.0.0/0 -> next hop AzFW
Add a static route to route table
0.0.0.0/0 -> next hop AzFW

## Slide 21: Custom use case – Route through NVA
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
10.1.0.0/24 | VNet1 Conn ID
10.3.0.0/24 | VNet3 Conn ID
10.2.0.0/24 | VNet2 Conn ID
10.4.0.0/24 | VNet4 Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
192.168.1.0/24 | S2S VPN Conn ID
192.168.2.0/24 | ER Conn ID
192.168.3.0/24 | S2S VPN Conn ID
192.168.4.0/24 | ER Conn ID
Default Route Table – Label Default | 
Route | Next hop
Default Route Table – Label Default | 
Route | Next hop
Ensure UDR from indirect spoke to the NVA VNETs
1
192.168.1.0/24
192.168.2.0/24
VNet1
VNet2
10.1.0.0/24
10.2.0.0/24
10.2.0.5
192.168.3.0/24
192.168.4.0/24
VNet3
VNet4
10.3.0.0/24
10.4.0.0/24
10.4.0.5
VNet2a
VNet2b
10.2.1.0/24
10.2.2.0/24
VNet4a
VNet4b
10.4.1.0/24
10.4.2.0/24
1
VNET2 Connection
VNET4 Connection
Ensure Static route to get to NVA connections
Add a static route
10.2.0.0/16 -> next hop VNet2 conn ID
10.4.0.0/16 -> next hop VNet4 conn ID
2
2
Add a static route
10.2.0.0/16 -> next hop VNet2 conn ID
10.4.0.0/16 -> next hop VNet4 conn ID
Enter the NVA IP in the NVA Connection
3
3
Internet
Routing Configuration – VNETs , Branches
Association Default
Propagation Default

## Slide 22: Virtual WAN Portal
Create route table

## Slide 23: Virtual WAN Portal
Basics : Set up static route in this route table with next hop
Azure Firewall
VNET connection ID

## Slide 24: Virtual WAN Portal
Label : Set up label to propagate routes across multiple route tables

## Slide 25: Virtual WAN Portal
Associations : Select connections =>these connections will learn routes from this route table
All connections associate always to a single route table

## Slide 26: Virtual WAN Portal
Propagations : Select connections to propagate routes to this route table
Connections can propagate to multiple route tables
Branch connections propagate to the ‘same set’ of route tables

## Slide 27: Virtual WAN Portal
View effective routes of a route table

## Slide 28: Let’s summarize – Routing
1. S2S, P2S, ExpressRoute connections are considered as branch spokes
Associate to default route table
Propagate to the ‘same set’ of route tables
2. Custom route tables are currently supported only for VNets
3. Connections associate to a route table =>they learn routes from that route table
4. Connections propagate routes to a route table <= the route table learns about the connection
5. Specific routes always win [e.g 10.1.0.0/24 is more specific than 10.0.0.0/16]
6. Set up static route with next hop as AzFW , VNet Connection ID
7. View effective routes on route tables
8. Connections propagate to none (label)/none route table => Black hole

## Slide 29: Integrated Virtual Appliance – Cisco Viptela demo
Supports transit
SASE : Works with Secure Virtual Hub
Built-in resiliency
No hassle routing
Virtual Hub Router
VPN Gateway
ExpressRoute Gateway
User VPN Gateway
Azure Firewall
Network Virtual Appliance

## Slide 30: Cisco Viptela demo video placeholder
Insert partner video here

## Slide 31: To summarize
Azure Virtual WAN provides ubiquitous connectivity, routing and security in a unified framework

## Slide 32: Resources
Microsoft announcement blog?
aka.ms/virtualwan-docs

## Slide 33: Thank you